## Slide 1: 1H NMR spectroscopy

## Slide 2: Theory & Principle of NMR
In the late 1940’s, physical chemists originally developed NMR spectroscopy to study different properties of atomic nuclei, but later found it to be useful in determining the molecular structure of organic compounds.
The theory behind NMR comes from the spin, I of a nucleus. Just as electrons have a +1/2, -1/2 spin, certain nuclei also experience charged spins that create a magnetic field (called the magnetic moment), which allows chemists to study them using NMR. Nuclei with even numbers of both neutrons and protons experience NO spin and nuclei with odd numbers of both neutrons and protons have integer spins. Nuclei that have the sum of protons and neutrons equal to an odd number (like 1 H and 13C) have half-integer spins.

## Slide 4
When there is no external or applied magnetic field (B0), the nuclear spins orient randomly; however, when there is an applied magnetic field, the nuclei orient themselves with or against the larger applied field. The α-spin state is parallel to the applied force and has lower energy than the β- spin state that is antiparallel to the applied force. The energy difference (δE) between the α- and β-spin states depends on the strength of the applied magnetic field. The greater the strength of the applied magnetic field, the greater is the δ E between the α- and β-spin states. The δ E between the α- and β-spin state is ~0.02 cal mol-1, which lies in the radio frequency region. The emitted energy in this region produces an NMR signal.

## Slide 5: Instrumentation:

## Slide 6
Components of 1H-NMR spectrometer
Magnet: Three types of magnets have been used in NMR spectrometers; these are
permanent magnet, electromagnet and super conducting solenoid.
The Sample Probe: It is a key component in NMR spectrometer which not only holds the sample in a fixed position in the magnetic field but also contains an air turbine to rotate (spin) the sample
Detector System: High frequency radio signal is first converted to an audio frequency signal which can be thought of as being made up of two components; a carrier signal which has the frequency of the oscillator that is used to produce it and a superimposed NMR signal from the analyte.
Sample Handing: In general, high resolution NMR spectroscopy work requires clear transparent sample solution of 2 to 15% concentration.
Representation of NMR
The NMR spectrum is recorded on a chart paper with X-axis representing chemical shift (ð) in ppm and Y-axis as intensity. The δ values increase from right to left. The value of zero on the X-axis corresponds to the internal standard, tetramethylsilane (TMS) signal. As you have learnt earlier, the low ð values correspond to high and vice versa. The NMR spectra are normally recorded in two modes; absorption and integral modes. The output consists of two traces – one is the spectrum i.e., the absorption signals at different d values and the other called integration trace.

## Slide 7: NMR Spectrum
The NMR spectrum is plot of intensity of NMR signal versus the magnetic field frequency in reference to TMS. The intensity is measured by integration of area under the triangles.

## Slide 8: Interpreting 1H NMR Spectra:
The Information’s obtained from 1H –NMR are: 1) CH3-CH3
2) CH3CH2OH
1) Number of signals:
Protons within a compound experience different magnetic environments, which give a separate signal in the NMR spectrum.
Equivalent Protons that reside in the same magnetic environment are termed chemically equivalent protons.
Examples, As a general rule of thumb, H’s in CH3 and CH2 groups are usuallyequivalent. Symmetrical compounds, such as benzene, are also equivalent.
However, since many compounds are not symmetrical, it is important to know how to identify nonequivalent protons. Protons that are different in any way (even in their stereochemistry) are not equivalent and will absorb at different frequencies (give a separate signal on the NMR spectra).

## Slide 10
2) Position of signals (chemical shift):
The position on the horizontal frequency scale at which the equivalent proton signals occur (δ E) is called a chemical shift (measured in δ ppm). Protons generally sense 3 different magnetic fields: magnetic field of the Earth, the NMR spectra, and different protons in the molecule. Since the magnetic fields of the Earth and NMR spectra are felt similarly by all the protons in the molecule, the chemical shift depends only on the varying local magnetic fields from the neighboring protons.
The chemical shift parameter δ is defined δ = (Hr – Hs)/Hr × 106 ppm
where Hr and Hs are field strengths corresponding to resonance for a particular nucleus in the sample (Hs) and reference (Hr).
But as spectra are usually calibrated in cycles per second (cps), the equation can be written as:
δ = ∆v × 106/Oscillator frequency (cps)
where ∆v = Difference in absorption frequencies of the sample and the reference in cps; oscillator frequency is the characteristic of the instrument: For a 60 MHz instrument, the oscillator frequency is 60 × 106 cps.
The factor 106 has been included for convenience.

## Slide 11
3) Reference compound: Tetramethylsilane (TMS)
In order to standardize the NMR spectra, the chemical shifts are positioned in relation to a reference proton set at 0.00 ppm. Tetramethylsilane, (CH3)4Si, is the standard for 1H NMR. TMS is practical as a reference compound because of its inert quality that prevents it from reacting with the sample and its highly volatile nature that makes it easy to evaporate out of samples. Few compounds have a lower frequency reading than TMS and it has 12 equivalent protons that read strongly on the NMR spectra.

## Slide 12
4) Shielding effects:
Under an applied magnetic field, circulating electrons in the electron cloud produce a small opposing magnetic field, ultimately decreasing the effective magnetic field felt by the proton, shifting the signal to the right (or upfield). This effect, in which the electron cloud “shields” the proton from the applied magnetic field is called local diamagnetic shielding.

## Slide 13
5) Electronegativity and deshielding:
Hydrogen atoms that are attached to more electronegative atoms experience higher chemical shifts. Electronegative atoms also remove electrons from the electron cloud, which decreases their density and results in less shielding; hence electronegative atoms are said to deshield the proton and cause it to have a higher chemical shift, moving it to the left (or downfield). The magnitude of the deshielding effect, however, rapidly decreases as the distance between the proton and electronegative atom increases (refer to NMR spectrum diagram above).
Examples: Literature values of the methyl chemical shift as it moves away from bromine

## Slide 14
6) Relative Intensity of Signals (Integration):
The area under the signals (integration) corresponds to the number of protons responsible for that signal. Therefore, the relative intensities of the signal are proportional to the relative number of proton equivalents. It is important to remember that integration only provides ratios of protons, not the absolute number. For convenience in calculating the relative signal strengths, the smallest integration is set to 1 and the other values are converted accordingly.

## Slide 15
7) Splitting of signals (spin-spin coupling):
NMR signals are not usually single triangles, but a complex pattern of split triangles labeled as doublets (2 peaks), triplets (3 peaks), quartets (4 peaks), etc. The distance between the split peaks are called coupling constants, denoted by J13. The interaction between nearby protons produce different spin flip energies (_ E) as they can orient themselves in a pattern of parallel or antiparallel to the applied magnetic force. This phenomenon, where the spin of the nucleus of one proton is close enough to affect the spin of another, is called spin-spin coupling. Splitting is always reciprocated between the protons—if Ha splits Hb, then Hb must split Ha—and provides information on the neighbors of a proton within the molecule.

## Slide 16: When high MHz mangnet NMR is used
CH3-CH2-OH Ethanol
formula for splitting is n+1
Triplet for CH3 1:2:1
Querter for CH2 1:3:3:1
CH3-CH2-CH2-OH
CH3- 2neighboring proton hence triplet
CH2- 5 neighbouring protons hence hexet
CH2- 2 neighbouring protons hence triplet.
CHa3-CHb(CHc3)-CHd2-CHe3
Ha- 1 neighbouring proton hence doublet
Hb – 8 neighbouring protons hence nine peaks
Hc- 1 neighbouring proton hence doublet
Hd- 4 neighbouring protons hence pentet
He – 2 neighbouring protons hence triplet.

## Slide 17
Factors affecting the chemical shift:
Actually the chemical shift parameter δ is a function of electron density around the nucleus as the electrons are directly involved in the diamagnetic shielding which acts to attenuate the applied magnetic field. Hence following factors are responsible for influencing its value:
(a) Specific solvent,
(b) Bulk diamagnetic susceptibility effect,
(c) Temperature (only when change in temperature causes changes in some type of association equilibrium or changes in amplitude of torsional vibrations),
(d) Electron density,
(e) Inductive effect,
(f) Vander Waal deshielding, and
(g) Hydrogen bonding.

## Slide 18
Applications of N.M.R. Spectroscopy:
Quantitative Analysis:
  The area of peak is directly proportional to the number of nuclei responsible for that peak. Thus the concentration of species can be determined directly by making use of signal area per proton. The signal area per proton can easily be calculated by use of a known concentration of an internal standard.
Similarly, (the concentration of new species formed during the reaction can also be calculated from the spectrum of parent compound.
(2) Qualitative Analysis:
The qualitative analysis of the compound can easily be made by knowing:
(i) Chemical shift delta values of hydrogen containing groups,
(ii) The presence of particular functional group,
(iii) The relative position of these groups and
(iv) The relative number of nuclei in these groups.