## Slide 1: FUEL CELLS

## Slide 2: FUEL CELLS
A fuel cell is an electrochemical device that produces electricity without combustion by combining hydrogen and oxygen to produce heat and water

## Slide 3: History of Fuel Cells
Discovered by German scientist G.H.Shoenbein.
First developed by William Grove.
Developed by Grove while conducting research on electrolysis.
Between 1930s to 1950s, British engineer Francis Thomas Bacon worked on developing alkaline fuel cells.
He demonstrated a working stack in 1958
The technology was licensed to Pratt and Whitney where it was utilized for Apollo spacecraft fuel cells

## Slide 4: Advantages of Fuel Cells over conventional energy sources
They produce zero or very low emissions, especially Green House Gases depending on the fuel used.
Efficiency of fuel cells is more than efficiency of conventional heat engines.
They have an excellent response time.
They require minimal maintenance.
No recharging is required.

## Slide 5: Structure of Hydrogen fuel cell
2H2 + 4OH – (aq)  4H2O
O2 + 2H2O + 4e-  4OH-
-------------------------------------------------
2H2 + O2  2H2O

## Slide 6: Working Principle-
A fuel cell is a device which uses Hydrogen (or a hydrogen rich fuel) and oxygen to create electricity by an electrochemical process.
A single fuel cell consists of an electrolyte sandwiched between two electrodes (a porous anode and cathode.)
Hydrogen or a hydrogen rich fuel is fed to the anode where a catalyst separates hydrogen’s negatively charged electrodes from positively charged ions (protons).
At the cathode, the oxygen combines with the electrons and, in some cases, with species like protons or water, resulting in water or hydroxide ions, respectively.

## Slide 7
The electrons from anode side of the cell cannot pass through the membrane to the positively charged cathode; they must travel around it via an electrical circuit to reach the other side of the cell. The movement of the electrons is an electrical current
This is how generation of electric current takes place via a fuel cell

## Slide 8: Factors on which Power generated depends
The power generated by fuel cell depends on factors such as:
Fuel cell type.
Cell size.
Temperature at which it operates.
Pressure at which the gases are supplies to the cell.

## Slide 9: Diagram of an alkaline fuel cell

## Slide 10: Alkaline fuel cells
Alkaline fuel cells use an alkaline electrolyte such as 40% aqueous potassium hydroxide.
In alkaline fuel cells travel through the electrolyte to the anode where they combine with the anode to form water and electrolyte
These fuel cells use a solution of potassium hydroxide in water as the electrolyte and can use a variety of non precious metals as a catalyst at the anode and cathode.
High temperature AFCs operate between 373K-523K.
However more recent AFCs operate at lower temperatures between 296K-343K.

## Slide 11: Advantages
The efficiency is as high as 60%
Cathode reaction is faster in an alkaline electrolyte; thus leading to high performance.
Disadvantages
This cell is easily poisoned by CO2.
Even the smallest amount of CO2 in air can affect the performance of the cell’s operation, making it necessary to purify both the hydrogen and oxygen used in the cell.
Susceptibility to poisoning reduces cell’s lifetime.

## Slide 12
Applications of fuel cells
Fuel cells are very useful in remote locations, such as spacecraft, remote weather stations, rural locations including research stations, and in certain military applications.
As of 2015, two fuel cell vehicles have been introduced in commercial market in limited quantities: the Toyota Mirai and the Hyundai ix35 FCEV. Additional demonstration models include the Honda FCX Clarity, and Mercedes-Benz F-Cell

## Slide 13
As of August 2011, there were a total of approximately 100 fuel cell buses deployed around the world.
In 2013 there were over 4,000 fuel cell forklifts used in material handling in the US.
In 2005 a British manufacturer of hydrogen-powered fuel cells, Intelligent energy, produced the first working hydrogen run motorcycle called the Emission Neutral Vehicle. The motorcycle holds enough fuel to run for four hours, and to travel 160 km (100 mi) in an urban area, at a top speed of 80 km/h (50 mph)
Hyundai Nexo
Toyota Mirai

## Slide 14: Advantages of fuel cells
  Hydrogen being the most abundant element in the universe, makes hydrogen fuel cells more viable
  Hydrogen has the highest energy content.
  Hydrogen is non polluting
  Reduces dependency on fossil fuels

## Slide 15: Disadvantages of fuel cells
Hydrogen is very expensive, not because it is rare but because its difficult to generate, handle and store requiring bulky tanks like those for CNG.
It can be stored at moderate temperatures and pressures in a tank containing a metal-hydride absorber or or carbon absorber, but both of these are very expensive.
Fuel cells are often very bulky and can not be used everywhere.
The actual cells in which power generated is stored can store only a small amount of power. This reduces the reliability of the entire process